## Slide 1: Midterm Project Presentation
Yu Feng and Luke Allen

## Slide 2: Problem
The problem we were tasked with for our midterm project is to create a behavioral model for the entire MSDAP chip as it is described in the MSDAP paper and given specification.
Our assigned input and output modes are as follows:
Input data: Serial
Output data: parallel
start: Active high
frame: active high
reset_n: active low.

## Slide 3: Top Level FSM
State 0
Initialization
State 1
Waiting to receive Rj
State 2
Receiving all Rj
State 3
Waiting to receive coefficients
State 4
Reading all coefficients
State 5
Waiting to receive input data
State 6
State 7
Reset
State 8
Sleep
CalcL
CalcR
reset_n
reset_n
reset_n
reset_n
non-zero input on inDataL or inDataR
800 consecutive zeros on both inDataL and inDataR
start

## Slide 4: Calculation FSM
Reset
State 0
Calculate Uj
State 2
Result Ready
resetCalc
State 1
Shifting Result
resetCalc
resetCalc
!resetCalc
All Rjs have not been used
All Rjs used
Calculated all coeff for this Rj

## Slide 5: Modules
MSDAP
sClk
dClk
start
reset_n
frame
inDataL
inDataR
inReady
outReady
outDataL
outDataR
Inputs
Outputs
40
40
Calculation
sClk
resetCalc
inData
inCoeffSign
rjIn
endCoeffIndex
readyForData
currentRjIndex
thisNcompleted
overallResult
Inputs
Outputs
40
4
16
10
16
CalcL
CalcR
reqNewEndCoeff

## Slide 6: Reading Data
always @ (negedge dClk)
if(inReady)
if(frame)
readFlag = 1
bit index = 15
read first bit and save at bit index
bitindex--
else
if(readflag)
read bit and save at bit index
if(bit index == 0)
readFlag = 0
if(state == 2)
save in Rj array at rjIndex
if(rjIndex == size of rj)
done
else
rjIndex++
if(state == 6)
save data to array at dataIndex
done
dataIndex++
else
bitIndex--

## Slide 7: State 6
If(state == 6)
inReady = 1 //inReady set to 1
if(input data is done recieving)
done = 0
resetCalc = 1 //Bring calc modules out of reset mode
if(both channels have 0)
zerocount++
else
zerocount = 0
if(zerocount == 800)
state = 8;
if(both channels have completed calculation)
outData = output from calc //Capture output
resetCalc = 0 //Reset calculation module
outReady = 1 //set outReady high
endCoeffIndex = 0 //Reset endCoeffIndex
delay //Delay some time for reset
resetCalc = 1 //Set resetCalc back to 1

## Slide 8: Calculation
always @ (posedge sClk or negedge resetCalc)
if(!resetCalc)
reset
else if(state == 0)
readyForData = 1
sign extend data to 24 bit
if(coeff is negative)
twos compliment
extend data to 40 bit
add this result to currentUjOut
readyForData = 0
currentCoeffIndex++
if(currentCoeffIndex == endCoeffIndex)
state = 1
else if(state == 1)
add currentUjOut to overallResult
shift right one bit, and pad MSB with sign bit
currentRjIndex++
request new endCoeffIndex
if(currentRjIndex == size of Rj)
state = 2
else
currentUjOut = 0;
state = 0
else if(state == 2)
thisNcompleted = 1 and hold until reset

## Slide 9: Communication with Calc Module
always @ (negedge readyForData)
if(calculation module is not is reset)
coeffExtracted= coeff[CoeffIndex]
coeffSign = sign bit of coeffExtracted
coeffValue = rest of coeffExtracted dataIndextoFetch = n – Coeffvalue
dataInput = data[dataIndextoFetch]
coeffIndex++

## Slide 10: Requesting new end coefficient Index
always @ (negedge requestNextEndCoeff)
endCoeffIndex = Rj[rjIndex] + endCoeffIndex

## Slide 11: Writing Outputs
always @ (posedge sClk and outReady)
pass output of calc module to output of FSM
outReady = 0